## Slide 1
Landscape: precedent research
AI AUTONOMOUS OPERATION PROPOSAL · LANDSCAPE
RHEED online analysis
PNNL — Pacific Northwest National Laboratory (US DOE; Kaspar et al.). Built RHAAPsody: unsupervised, material-agnostic on-the-fly RHEED analysis — pretrained-CNN features, changepoint detection, graph clustering. On live TiO2 MBE growth: <1 s/frame, transitions flagged ~1 min faster than the human expert. Open source; perception only — control is their stated next phase.
JVST A 43, 032702 (2025)
GitHub: pnnl/RHAAPSODY
MBE real-time closed loop
Chinese Academy of Sciences (Shen et al.); follow-up QD-laser work. 3D ResNet-50 on RHEED video predicts InAs/GaAs quantum-dot density in-run; the closed loop dials density across 3.8×10⁸–1.4×10¹¹ cm⁻² (~2.5 orders of magnitude), fully automated. The 2025 follow-up self-optimizes QD-laser growth: PL 3.2× the manual baseline, ~0.85 s per decision.
Nat. Commun. 15, 2724 (2024)
QD-laser (2025, PMC)
MBE unattended operation
IVWorks — Korean GaN epiwafer foundry. DOMM Agent drives the MBE control PC: scheduled load–grow–unload runs execute unattended on nights/holidays with real-time pass/fail prediction. Commercial existence proof of the route — no yield / unattended-hours / dispersion figures published; cite strictly as a vendor claim.
IVWorks announcement (Jun 2025)
Autonomous experimentation, real sputter tool
Empa — Swiss Federal Laboratories for Materials Science & Technology (Wieczorek, Siol et al.). Autonomous Bayesian sampling (BayBE / BoTorch GP) on a real bipolar-HiPIMS rig: >3,000 conditions across a 6-D space, unattended, SHAP-interpreted, data CC-BY. Their own finding was negative (positive pulse mostly hurts rate) — we cite method + dataset; our RIG kernel passed calibration acceptance on exactly this dataset.
Digital Discovery (2026)
Zenodo dataset (CC-BY-4.0)
Self-driving PVD to a target spec
npj Computational Materials (2025) — self-driving sputter lab. Fully autonomous silver-film deposition: sputter hardware + in-situ optical spectroscopy + Bayesian ML with no human in the loop, aborting unpromising runs early. Hit the target optical spec in 2.3 attempts on average (vs 3.6 ablated), 98 s per cycle, >20,000 data points over 38 samples.
npj Comput. Mater. (2025)
Run-to-run APC + virtual metrology
Industry practice (PVD). Published sputter-APC case: EWMA run-to-run compensation of target-erosion drift lifts Cpk from <1.4 to >2.0 — a retrospective simulation on historical fab data (vendor case study, not audited). Tree-ensemble virtual metrology for PVD film properties: Chen et al., ISA Trans. 103 (2020).
Spotfire sputter-APC article
Notes: Sourcing caveats — state these if challenged on any figure: • IVWorks DOMM: vendor marketing only. No published yield, unattended-hours or dispersion numbers. Cite as existence proof of the commercial route, never as a numeric benchmark. DOMM is not sold externally. • Empa (Digital Discovery 2026): the paper's own scientific conclusion is negative — positive pulsing is broadly unfavourable for deposition rate. We cite the autonomous methodology and the real dataset, not any claim that autonomy improves rate. • Sputter APC Cpk <1.4 → >2.0 is a vendor case study in retrospective simulation, not an audited result. • The commonly cited estimate that APC is worth >US$300M/yr to a 20K wafer/month logic fab is a consultancy figure, not independently audited. Quote it only with that qualification. • RHAAPsody is a perception benchmark. It does not perform active control; our pipeline extends its methodology.

## Slide 2
Problem definition
AI AUTONOMOUS OPERATION PROPOSAL · PROBLEM DEFINITION
Process quality on MBE and PVD still rests on the operator's judgement in the moment: RHEED is read by eye; PVD drift is compensated by spot checks and experience.
1
Latency
A human reacts to an anomaly in minutes. Growth-stage transitions — AlN nucleation giving way to streak recovery — open and close in seconds.
2
Not reproducible
The same recipe spreads across shifts and operators. That spread is one of the main sources of yield loss.
3
Does not scale
Doubling capacity means doubling skilled engineers — and skilled engineers cannot be produced on that schedule.
OBJECTIVE
Run the equipment unattended: judge process state from in-situ signals, correct the control variables, and turn engineering intuition into an auditable, reusable software asset.
WHAT “AUTONOMOUS AGENT” MEANS HERE — THE STRICT DEFINITION
Sense
→
State estimate
(uncertainty)
→
Decide
→
Independent
check
→
Bounded
action
→
Full audit
trail
→
Learn &
refit
DATA FLYWHEEL · EVERY AUDITED RUN RETURNS AS TRAINING DATA — THE LOOP SHARPENS ITSELF
Every link carries an acceptance gate. Outside its competence the system returns INFEASIBLE with a diagnosis — it never forces an answer.
Notes: Three manufacturing problems, the strict definition of autonomy used in this proposal, and the data flywheel that compounds across runs.

## Slide 3
Target intelligent autonomous workflow
AI AUTONOMOUS OPERATION PROPOSAL · TARGET WORKFLOW
RUN-TO-RUN
recipe-level learning
IN-SITU
second-level sensing
EX-SITU
post-run metrology
Data model (RIG)
learns past recipes + outcomes; calibrated forward model; optimizes the next recipe for MBE and PVD
Equipment — MBE / PVD
control + monitoring; MBE in-run control via RHEED pipeline; PVD in-situ per available sensors
Measurement
thickness, uniformity, sheet resistance, stress — joined back to each run
optimized recipe
output wafer
run data
in-run loop
LOCAL LLM
orchestrator · wraps the whole process
reason · instruct · audit
writes only via whitelisted, gated actions
reason over runs
instruct (bounded)
read results
Notes: Target loop: the data model proposes a recipe, the equipment runs it under in-situ RHEED sensing, measurement feedback returns to the model; the local LLM reasons over the run and issues control.

## Slide 4
Existing foundation: in-house software
AI AUTONOMOUS OPERATION PROPOSAL · EXISTING FOUNDATION
01
DATA MODEL
Recipe-Inverse Generator (RIG)
A forward model from recipe to result plus an inverse solver that back-calculates candidate recipes to meet a requirement — with calibrated uncertainty and honest refusal (INFEASIBLE + diagnosis).
VERIFIED
Passed calibration acceptance on Empa's real magnetron-sputtering HiPIMS (PVD) dataset.
NEXT
Validation on our own tool data.
02
SENSING AND CONTROL
RHEED Analysis
A CNN + ViT computer-vision pipeline for in-situ image analysis and monitoring: finds transition points and anomalies; an LLM co-pilot interprets and suggests actions.
VERIFIED
Runs end-to-end on two sets of real TiO2 RHEED data; fault-injection evaluation quantifies latency, attribution and false alarms.
NEXT
GaN RHEED validation + tool validation.
03
PHYSICAL SIMULATION
MBE Simulation
A physics-based simulation model of the MBE chamber: flux geometry, surface kinetics, thermal model and a live machine model.
VERIFIED
Underlying physics built out and refined (literature-anchored calibration).
NEXT
Calibration against real tool data.
Notes: Current status and next step for the three in-house assets; none has yet been validated on this project's own tool.

## Slide 5
Autonomy ladder and engineering specification
AI AUTONOMOUS OPERATION PROPOSAL · AUTONOMY ROADMAP
SCOPE
ENTRY CONDITIONS — QUALITATIVE FOR NOW; NUMERIC GATES SET AFTER BASELINE MEASUREMENT
L1
Observe
Read-only acquisition; full data capture during runs.
Data contract accepted: every signal captured with trustworthy time synchronisation; the ingest validation layer proven by fault injection to actually reject bad data.
L2
Shadow
AI issues decisions with rationale; nothing is written to the tool.
Model calibration passes its acceptance check on our own tool data; perception agrees with expert judgement consistently across a sustained shadow period.
L3
Supervised loop
Single variable, then multivariable (MBE, PVD); one-click engineer takeover at every step.
Control law clears the full fault-injection suite in simulation; write-back latency verified against fast-loop needs; watchdogs and clamps proven in red-then-green drills; every recipe change passes the independent confirmation gate.
L4
Unattended
Continuous unattended operation.
Supervised operation stable over a sustained period; EHS and insurance sign-off in writing; unattended and fallback drills (network loss, heartbeat loss, sensor failure) all passed.