## Slide 1
AI-driven Autonomous Deposition Lab
Project proposal
29 July 2026

## Slide 2
Problem definition
AI AUTONOMOUS OPERATION PROPOSAL · PROBLEM DEFINITION
Process quality on MBE and PVD still rests on the operator's judgement in the moment
01
Latency
A human reacts to an anomaly in minutes. Changes during growth happen in seconds
02
Not reproducible
The same recipe spreads across shift. Procedure judgement different across operators.
03
Does not scale
Experienced engineers cant be increased linearly at the same rate
OBJECTIVE
Autonomous operation + closed feedback loop
turning engineering intuition into an quantifiable, reusable software asset
AUTONOMOUS AGENT
Sensor
State prediction
Decision
Verification
Bounded
action
Full audit
log
Learn &
refit

## Slide 3
Landscape: current examples
AI AUTONOMOUS OPERATION PROPOSAL · LANDSCAPE
1
AI-Driven Epitaxy
(Paul-Drude-Institute)
(Jun 2026)
UnicornOne: vendor-agnostic LabOS unifying hardware, time-resolved RHEED and workflows. Real + synthetic RHEED simulation data trained hybrid multi-model AI for GaN growth. Time savings were translating into saving ~€55k/yr/system
MBE agentic operation
(IVWorks)
(Jun 2025)
Korean GaN epiwafer foundry. DOMM Agent drives the MBE control PC: scheduled load–grow–unload runs execute unattended on nights/holidays with real-time pass/fail prediction. no detail/yield/dispersion figures published
Self-driving PVD lab
(University of Chicago)
(2025)
Autonomous PVD lab using robotics, in-situ optical spectroscopy, and Gaussian Process Regression ML. Uses a initial calibration layer to account for hidden chamber/substrate variations, optimizing silver film deposition to target optical specs in ~2.3 attempts.(vs 3.6 ablated)
Run-to-run process control & virtual metrology
(Spotfire USA)
(2026)
Simulated run-to-run Advanced Process Control and Virtual Metrology for sputter deposition on synthetic fab data. Used linear target models + EWMA offsets to continuously adjust deposition time, counteracting target-erosion drift and lifting process quality (Process Capability Index from <1.4 to >2.0)
2
3
4

## Slide 4
Target workflow
AI AUTONOMOUS OPERATION PROPOSAL · TARGET WORKFLOW
RUN-TO-RUN
IN-SITU
EX-SITU
Data model
Database of past recipes outcome pairs; calibrated forward model + inverse solver for MBE and PVD for recipe optimization
Equipment
Process control + state monitoring; MBE in-situ control via RHEED pipeline; PVD in-situ per available sensors
Measurement
All output quality assessments (thickness, uniformity, sheet resistance, stress .etc)
optimized recipe
output wafer
Output
data
in-run loop
LOCAL LLM Orchestrator
Monitor
+ Control
Reasoning + Control
Infer results

## Slide 5
Autonomy roadmap and engineering specification
AI AUTONOMOUS OPERATION PROPOSAL · AUTONOMY ROADMAP
SCOPE
PASS CONDITIONS
L1
Acquisition
full data capture before, during and after runs
all signals captured with time synchronization with acceptable latency
specification and data format readable and validated
L2
Decision
Read-only AI decision making with reasoning
Model calibration against our own tool data
decisions agrees with expert judgement consistently
Controls clear all fault-injection tests in simulation
L3
Supervised
Supervised AI controlled operation
Machine controls all green and tested
write-back latency verified against fast-loop needs
operation stable over a sustained period & failure fallback drills passed
L4
Autonomous
Continuous autonomous operation
LEVEL
Zero human intervention required across full execution cycles
Yield/quality metrics equal or exceed human expert baselines

## Slide 6
Current foundation
AI AUTONOMOUS OPERATION PROPOSAL · EXISTING FOUNDATION
01
DATA MODEL
Recipe-Inverse Generator (RIG)
Forward model from recipe to result + inverse solver that back-calculates candidate recipes to meet requirements with uncertainty band and invalidation.
CURRENT
Tested and validated on Empa’s High Impulse magnetron-sputtering (PVD) dataset. Able to predict input from desired output
NEXT
Validation on our own tool & data.
02
SENSING AND CONTROL
RHEED Analysis Pipeline
CNN + ViT computer-vision pipeline for in-situ image analysis and monitoring
+ LLM based control system interprets and suggests/executes actions.
CURRENT
Tested on TiO2 RHEED data. Able to identify, analyze and suggest actions based on RHEED livestream
NEXT
Validation on GaN RHEED data
03
PHYSICAL SIMULATION
MBE Simulation
A physics-based simulation model of the MBE chamber: flux geometry, surface kinetics, thermal model and a estimated RHEED output display.
CURRENT
Underlying physics built and calibrated based on literature values
NEXT
Calibration against real tool data.